## Slide 1: Hand Gesture, Hand Shape and Articulated Hand Pose Recognition Using Depth Cameras
Cem Keskin1,2 Lale Akarun2
Boğaziçi University2

## Slide 2: Motivation
Human computer interaction
  Do everything that can be done with the hands
Sign language analysis
  Analyze and recognize gestures of any complexity

## Slide 3: Natural Interaction with Hands
Hand trajectory
Hand shape
Articulated hand pose

## Slide 4: Difficult to Capture Body Pose

## Slide 5: Until Kinect Came Along
Depth
Color

## Slide 6: How do Depth Cameras Work?
Stereo enables depth reconstruction if correspondence of points can be established
Projected Light enables correspondence matching

## Slide 7: How Does Kinect Work?
An infrared projector
A stereo infrared sensor
A color camera

## Slide 8: How Does Kinect Work?
The infrared pattern is sensed by the IF sensor
The color camera does not sense it

## Slide 9: Libraries for Kinect
PrimeSense – OpenNI
Microsoft Library
  Succesful body motion capture!

## Slide 10: Shotton et. al Body Pose Library
Uses a synthetic dataset of human motions with labeled body parts for training

## Slide 11: Shotton et. al Body Pose Library
Uses a Random Decision Forest to classify real images

## Slide 12: Shotton et. al Body Pose Library
Find Centroids using mean shift;
Connect the dots to get skeleton

## Slide 13: Motion Capture

## Slide 14: Kinect Applications
Notes: Kinect Uygulamaları

## Slide 15: Hand Gesture Recognition
Sigma NI
  OpenNI Developers challenge entry – 3rd place

## Slide 16: Recognition using Graphical Models
HMMs
IOHMMs
Mixtures of HMMs
CRF- HRCRF
EDM: Explicit Duration Models

## Slide 17: Breakthrough
Release of consumer depth cameras
Shotton et al.
  “Real-Time Human Pose Recognition in Parts from Single Depth Images” [CVPR 2011]
No library for hand!

## Slide 18: Adaptation to Hand Pose
Segment the hand into parts
Train RDFs and classify each pixel
Estimate the joints for each hand part
Create a hierarchical skeleton model
Connect the dots

## Slide 19: Challenges
Hand is much smaller in size than a body
Degree of freedom
  Body: 22-24 (ignoring feet and hands)
  Hand: 22
Self occlusion is severe and common
Hand is not always upright
Extremely hard to label real depth images

## Slide 20: On the other hand
Shape variation is much lower for different humans, especially for depth data

## Slide 21: Solution
Use synthetic images for training only
  Render depth images and ground truth labels
Stand closer to the camera
  Depends on the sensor depth image resolution
  Restrict the usage area to 80cm – 200cm

## Slide 22: Synthetic Dataset Generation

## Slide 23: Randomized Decision Forest
...
F
< τ
> τ
F
F
F
F
F
F
< τ
< τ
> τ
> τ

## Slide 24: Method Details
Depth invariant features (I: image, x: pixel):
Partitioning the data:

## Slide 25: Method Details
Score of the test is the information gain:
Posterior probabilities:

## Slide 26: Random Decision Forests
1 Tree
2 Trees
3 Trees

## Slide 27: Joint Estimation
Joints
Skeleton
20 Seeds
Scoring

## Slide 28: Proof of Concept: ASL Digits
Fit a skeleton, classify skeleton parameters
Generate synthetic dataset
Train RDF from dataset
Retrieve live stream
Fit a skeleton using RDF
Train SVM for ASL digits
Evaluate and classify

## Slide 29: Uses of Skeleton: Virtual Joystick
Turn the hand into an analog controller by imitating a joystick:
Estimates a 3D vector, and a distance for the click event

## Slide 30: Uses of Skeleton: Virtual Mouse
Turn the hand into a mouse by imitating the left click with a pinching gesture
Estimates a location and a distance to map into mouse coordinates and click events

## Slide 31: Hand Shape Recognition
Hand skeleton estimation method adapted to hand shape recognition problem
Simple idea: Label poses instead of hand parts

## Slide 32: Adapting to Hand Shape
Cluster hand shapes to form classes
Label each pixel
according to the hand shape label
Train Randomized Decision Forests & Classify each pixel
Collect real depth images for
different hand shapes
Determine the class label

## Slide 33: American Sign Language
Tested on a large dataset collected with Kinect (65k+ images)
  Pugeault et al. - Spelling It Out: Real Time ASL Fingerspelling Recognition – CDC4CV in ICCV 2011
Achieved 99.1% success rate with 3 trees, using only depth.
Extremely fast: 30 fps with 30 trees on the CPU

## Slide 34: SigmaNIL Framework

## Slide 35: SigmaNIL Framework
A visual toolset that aims to:
  Collect, split, merge and train datasets for all the supported modalities,
  Test the trained models concurrently in real time,
  Define events like mouse move or key press and bind them to gesture events to control 3rd party applications
It can be used to play games, control modeling or painting tools, understand sign language etc.

## Slide 36: SigmaNIL Advanced Capabilities
Recognize combinations of modalities:
  Trajectory + Shape
    Ex: Draw a circle while performing a “C”
  Trajectory + Skeleton
    Ex: Grab an object by pinching and draw a triangle to act
  Shape + Skeleton
    Ex: First check the shape to determine which skeleton expert to use. Joystick? Pinching? Generic hand skeleton?
  All three
    Determine pinching from shape and perform a gesture

## Slide 37: SigmaNIL Advanced Capabilities
Use both hands:
  Recognize two separate gestures,
  Use two joysticks, or a joystick and a mouse,
  Change the mode by performing a shape with the left hand, do something with the right hand, etc.
Unlimited flexibility for all kinds of scenarios

## Slide 38: Applications

## Slide 39: Questions?